## Slide 1: 2060 Regional Growth Scenarios for East-Central Florida
By Blake Harvey

## Slide 2: Project Description
A projection of future urban growth and development to 2060 in Brevard, Seminole, Volusia and Orange Counties

## Slide 3: Population Allocation Methodolgy
Determine land uses unlikely to change
  Conservation Lands
  Open Water
  Existing Urban Development
  Inundated Lands (in SLR scenarios)

## Slide 4: Population Projections
Determine new population to be added in four county region between 2010 and 2060
In SLR scenarios, add to this the population on land that will be displaced (assuming 100% stay in the study area)
Allocate some percentage to redevelopment in existing urban areas – the rest will be allocated to projected new development

## Slide 5: Determine Gross Urban Density
To determine new development density, the existing Gross Urban Density must first be calculated
First, the Gross Urban Area is calculated – in our scenarios, this was done with tax parcel data
Parcel classes that were determined to have urban structures, along with transportation networks, were considered the Gross Urban Area
This was then divided by the current population of the study area, for 5.406 people per acre

## Slide 6: Model Assumptions
 | Population to Allocate |  | Percent of New Population in Redevelopment |  | New Development Density |  | Available for Development |  | Not Available for Development
Trend Scenario | 2,523,310 |  | 0% |  | 5.406 People per Acre |  | Greenfield (Undeveloped) Lands, |  | Managed Lands, Transportation Networks, Water
2-Meter Sea Level Rise - Low Density | 2,005,077 |  | 25% |  | 5.406 People per Acre |  | Greenfield (Undeveloped) Lands, |  | Managed Lands, Transportation Networks, Water, Inundated Lands
2-Meter Sea Level Rise - High Density | 1,791,202 |  | 33% |  | 6.757 People per Acre |  | Greenfield (Undeveloped) Lands, |  | Managed Lands, Transportation Networks, Water, Inundated Lands
Three Scenarios were used:
  Low-Density “Trend” Scenario
  Low-Density Development/Sea Level Rise
  High-Density Development/Sea Level Rise

## Slide 7: Methodology
For sea level-rise scenarios, displaced population was calculated using 2-meter SLR models and census data, and this was added to the 2060 population growth, as population to allocate
All lands other than those for which the uses are not likely to change were considered developable “greenfield”
The amount of land projected to be developed (in acres) was calculated by dividing population growth by development density

## Slide 8: Methodology Continued
Population was allocated to specific acreage based on: “Developability” (greenfield), least land use conflict, and urban suitability
The level of urban suitability was used as a “threshold”

## Slide 9
High Urban Preference/No Conflict
Urban Suitability

## Slide 10: Results
  1. Low-Density “Trend” Scenario
  2. Low-Density Development/Sea Level Rise
  3. High-Density Development/Sea Level Rise

## Slide 11
Development Density: 5.406 People per Acre
Acres Projected for New Development: 494,812
Population Allocated to New Development: 2,674,958
Selection Criteria: Conflict 13, 12, 22, 23, 33, Urban Suitability over 265
Low-Density “Trend”

## Slide 12
Development Density: 5.406 People per Acre
Acres Projected for New Development: 370,801
Population Allocated to New Development: 2,004,527
Selection Criteria: Conflict 13, 12, 22, 23 Urban Suitability over 260
Low-Density/Sea Level Rise

## Slide 13
Development Density: 6.757 People per Acre
Acres Projected for New Development: 266,007
Population Allocated to New Development: 1,797,423
Selection Criteria: Conflict 13, 12, 23, Urban Suitability over 335
High-Density/Sea Level Rise

## Slide 14
Trend
High Density/SLR
Low Density/SLR